## Slide 1: Chapter 12 – Safety Engineering

## Slide 2: Topics covered
Safety-critical systems
Safety requirements
Safety engineering processes
Safety cases

## Slide 3: Safety
Safety is a property of a system that reflects the system’s ability to operate, normally or abnormally, without danger of causing human injury or death and without damage to the system’s environment.
It is important to consider software safety as most devices whose failure is critical now incorporate software-based control systems.

## Slide 4: Software in safety-critical systems
The system may be software-controlled so that the decisions made by the software and subsequent actions are safety-critical. Therefore, the software behaviour is directly related to the overall safety of the system.
Software is extensively used for checking and monitoring other safety-critical components in a system. For example, all aircraft engine components are monitored by software looking for early indications of component failure. This software is safety-critical because, if it fails, other components may fail and cause an accident.

## Slide 5: Safety and reliability
Safety and reliability are related but distinct
  In general, reliability and availability are necessary but not sufficient conditions for system safety
Reliability is concerned with conformance to a given specification and delivery of service
Safety is concerned with ensuring system cannot cause damage irrespective of whether or not it conforms to its specification.
  System reliability is essential for safety but is not enough
  Reliable systems can be unsafe

## Slide 6: Unsafe reliable systems
There may be dormant faults in a system that are undetected for many years and only rarely arise.
Specification errors
  If the system specification is incorrect then the system can behave as specified but still cause an accident.
Hardware failures generating spurious inputs
  Hard to anticipate in the specification.
Context-sensitive commands i.e. issuing the right command at the wrong time
  Often the result of operator error.

## Slide 7: Safety-critical systems

## Slide 8: Safety critical systems
Systems where it is essential that system operation is always safe i.e. the system should never cause damage to people or the system’s environment
Examples
  Control and monitoring systems in aircraft
  Process control systems in chemical manufacture
  Automobile control systems such as braking and engine management systems

## Slide 9: Safety criticality
Primary safety-critical systems
  Embedded software systems whose failure can cause the associated hardware to fail and directly threaten people. Example is the insulin pump control system.
Secondary safety-critical systems
  Systems whose failure results in faults in other (socio-technical) systems, which can then have safety consequences.
    For example, the Mentcare system is safety-critical as failure may lead to inappropriate treatment being prescribed.
    Infrastructure control systems are also secondary safety-critical systems.

## Slide 10: Hazards
Situations or events that can lead to an accident
  Stuck valve in reactor control system
  Incorrect computation by software in navigation system
  Failure to detect possible allergy in medication prescribing system
Hazards do not inevitably result in accidents – accident prevention actions can be taken.

## Slide 11: Safety achievement
Hazard avoidance
  The system is designed so that some classes of hazard simply cannot arise.
Hazard detection and removal
  The system is designed so that hazards are detected and removed before they result in an accident.
Damage limitation
  The system includes protection features that minimise the damage that may result from an accident.

## Slide 12: Safety terminology
Term | Definition
Accident (or mishap) | An unplanned event or sequence of events which results in human death or injury, damage to property, or to the environment. An overdose of insulin is an example of an accident.
Hazard | A condition with the potential for causing or contributing to an accident. A failure of the sensor that measures blood glucose is an example of a hazard.
Damage | A measure of the loss resulting from a mishap. Damage can range from many people being killed as a result of an accident to minor injury or property damage. Damage resulting from an overdose of insulin could be serious injury or the death of the user of the insulin pump.
Hazard severity | An assessment of the worst possible damage that could result from a particular hazard. Hazard severity can range from catastrophic, where many people are killed, to minor, where only minor damage results. When an individual death is a possibility, a reasonable assessment of hazard severity is ‘very high’.
Hazard probability | The probability of the events occurring which create a hazard. Probability values tend to be arbitrary but range from ‘probable’ (say 1/100 chance of a hazard occurring) to ‘implausible’ (no conceivable situations are likely in which the hazard could occur). The probability of a sensor failure in the insulin pump that results in an overdose is probably low.
Risk | This is a measure of the probability that the system will cause an accident. The risk is assessed by considering the hazard probability, the hazard severity, and the probability that the hazard will lead to an accident. The risk of an insulin overdose is probably medium to low.

## Slide 13: Normal accidents
Accidents in complex systems rarely have a single cause as these systems are designed to be resilient to a single point of failure
  Designing systems so that a single point of failure does not cause an accident is a fundamental principle of safe systems design.
Almost all accidents are a result of combinations of malfunctions rather than single failures.
It is probably the case that anticipating all problem combinations, especially, in software controlled systems is impossible so achieving complete safety is impossible. Accidents are inevitable.

## Slide 14: Software safety benefits
Although software failures can be safety-critical, the use of software control systems contributes to increased system safety
  Software monitoring and control allows a wider range of conditions to be monitored and controlled than is possible using electro-mechanical safety systems.
  Software control allows safety strategies to be adopted that reduce the amount of time people spend in hazardous environments.
  Software can detect and correct safety-critical operator errors.

## Slide 15: Safety requirements

## Slide 16: Safety specification
The goal of safety requirements engineering is to identify protection requirements that ensure that system failures do not cause injury or death or environmental damage.
Safety requirements may be ‘shall not’ requirements i.e. they define situations and events that should never occur.
Functional safety requirements define:
  Checking and recovery features that should be included in a system
  Features that provide protection against system failures and external attacks

## Slide 17: Hazard-driven analysis
Hazard identification
Hazard assessment
Hazard analysis
Safety requirements specification

## Slide 18: Hazard identification
Identify the hazards that may threaten the system.
Hazard identification may be based on different types of hazard:
  Physical hazards
  Electrical hazards
  Biological hazards
  Service failure hazards
  Etc.

## Slide 19: Insulin pump risks
Insulin overdose (service failure).
Insulin underdose (service failure).
Power failure due to exhausted battery (electrical).
Electrical interference with other medical equipment (electrical).
Poor sensor and actuator contact (physical).
Parts of machine break off in body (physical).
Infection caused by introduction of machine (biological).
Allergic reaction to materials or insulin (biological).

## Slide 20: Hazard assessment
The process is concerned with understanding the likelihood that a risk will arise and the potential consequences if an accident or incident should occur.
Risks may be categorised as:
  Intolerable. Must never arise or result in an accident
  As low as reasonably practical(ALARP). Must minimise the possibility of risk given cost and schedule constraints
  Acceptable. The consequences of the risk are acceptable and no extra costs should be incurred to reduce hazard probability

## Slide 21: The risk triangle

## Slide 22: Social acceptability of risk
The acceptability of a risk is determined by human, social and political considerations.
In most societies, the boundaries between the regions are pushed upwards with time i.e. society is less willing to accept risk
  For example, the costs of cleaning up pollution may be less than the costs of preventing it but this may not be socially acceptable.
Risk assessment is subjective
  Risks are identified as probable, unlikely, etc. This depends on who is making the assessment.

## Slide 23: Hazard assessment
Estimate the risk probability and the risk severity.
It is not normally possible to do this precisely so relative values are used such as ‘unlikely’, ‘rare’, ‘very high’, etc.
The aim must be to exclude risks that are likely to arise or that have high severity.

## Slide 24: Risk classification for the insulin pump
Identified hazard | Hazard probability | Accident severity | Estimated risk | Acceptability
1.Insulin overdose computation | Medium | High | High | Intolerable
2. Insulin underdose computation | Medium | Low | Low | Acceptable
3. Failure of hardware monitoring system | Medium | Medium | Low | ALARP
4. Power failure | High | Low | Low | Acceptable
5. Machine incorrectly fitted | High | High | High | Intolerable
6. Machine breaks in patient | Low | High | Medium | ALARP
7. Machine causes infection | Medium | Medium | Medium | ALARP
8. Electrical interference | Low | High | Medium | ALARP
9. Allergic reaction | Low | Low | Low | Acceptable

## Slide 25: Hazard analysis
Concerned with discovering the root causes of risks in a particular system.
Techniques have been mostly derived from safety-critical systems and can be
  Inductive, bottom-up techniques. Start with a proposed system failure and assess the hazards that could arise from that failure;
  Deductive, top-down techniques. Start with a hazard and deduce what the causes of this could be.

## Slide 26: Fault-tree analysis
A deductive top-down technique.
Put the risk or hazard at the root of the tree and identify the system states that could lead to that hazard.
Where appropriate, link these with ‘and’ or ‘or’ conditions.
A goal should be to minimise the number of single causes of system failure.

## Slide 27: An example of a software fault tree

## Slide 28: Fault tree analysis
Three possible conditions that can lead to delivery of incorrect dose of insulin
  Incorrect measurement of blood sugar level
  Failure of delivery system
  Dose delivered at wrong time
By analysis of the fault tree, root causes of these hazards related to software are:
  Algorithm error
  Arithmetic error

## Slide 29: Risk reduction
The aim of this process is to identify dependability requirements that specify how the risks should be managed and ensure that accidents/incidents do not arise.
Risk reduction strategies
  Hazard avoidance;
  Hazard detection and removal;
  Damage limitation.

## Slide 30: Strategy use
Normally, in critical systems, a mix of risk reduction strategies are used.
In a chemical plant control system, the system will include sensors to detect and correct excess pressure in the reactor.
However, it will also include an independent protection system that opens a relief valve if dangerously high pressure is detected.

## Slide 31: Insulin pump - software risks
Arithmetic error
  A computation causes the value of a variable to overflow or underflow;
  Maybe include an exception handler for each type of arithmetic error.
Algorithmic error
  Compare dose to be delivered with previous dose or safe maximum doses. Reduce dose if too high.

## Slide 32: Examples of safety requirements
SR1: The system shall not deliver a single dose of insulin that is greater than a specified maximum dose for a system user.
SR2: The system shall not deliver a daily cumulative dose of insulin that is greater than a specified maximum daily dose for a system user.
SR3: The system shall include a hardware diagnostic facility that shall be executed at least four times per hour.
SR4: The system shall include an exception handler for all of the exceptions that are identified in Table 3.
SR5: The audible alarm shall be sounded when any hardware or software anomaly is discovered and a diagnostic message, as defined in Table 4, shall be displayed.
SR6: In the event of an alarm, insulin delivery shall be suspended until the user has reset the system and cleared the alarm.

## Slide 33: Safety engineering processes

## Slide 34: Safety engineering processes
Safety engineering processes are based on reliability engineering processes
  Plan-based approach with reviews and checks at each stage in the process
  General goal of fault avoidance and fault detection
  Must also include safety reviews and explicit identification and tracking of hazards

## Slide 35: Regulation
Regulators may require evidence that safety engineering processes have been used in system development
For example:
  The specification of the system that has been developed and records of the checks made on that specification.
  Evidence of the verification and validation processes that have been carried out and the results of the system verification and validation.
  Evidence that the organizations developing the system have defined and dependable software processes that include safety assurance reviews. There must also be records that show that these processes have been properly enacted.

## Slide 36: Agile methods and safety
Agile methods are not usually used for safety-critical systems engineering
  Extensive process and product documentation is needed for system regulation. Contradicts the focus in agile methods on the software itself.
  A detailed safety analysis of a complete system specification is important. Contradicts the interleaved development of a system specification and program.
Some agile techniques such as test-driven development may be used

## Slide 37: Safety assurance processes
Process assurance involves defining a dependable process and ensuring that this process is followed during the system development.
Process assurance focuses on:
  Do we have the right processes? Are the processes appropriate for the level of dependability required. Should include requirements management, change management, reviews and inspections, etc.
  Are we doing the processes right? Have these processes been followed by the development team.
Process assurance generates documentation
  Agile processes therefore are rarely used for critical systems.

## Slide 38: Processes for safety assurance
Process assurance is important for safety-critical systems development:
  Accidents are rare events so testing may not find all problems;
  Safety requirements are sometimes ‘shall not’ requirements so cannot be demonstrated through testing.
Safety assurance activities may be included in the software process that record the analyses that have been carried out and the people responsible for these.
  Personal responsibility is important as system failures may lead to subsequent legal actions.

## Slide 39: Safety related process activities
Creation of a hazard logging and monitoring system.
Appointment of project safety engineers who have explicit responsibility for system safety.
Extensive use of safety reviews.
Creation of a safety certification system where the safety of critical components is formally certified.
Detailed configuration management (see Chapter 25).

## Slide 40: Hazard analysis
Hazard analysis involves identifying hazards and their root causes.
There should be clear traceability from identified hazards through their analysis to the actions taken during the process to ensure that these hazards have been covered.
A hazard log may be used to track hazards throughout the process.

## Slide 41: A simplified hazard log entry
Hazard Log Page 4: Printed 20.02.2012 |  |  |  |  |  | 
System: Insulin Pump System Safety Engineer: James Brown |  |  |  | File: InsulinPump/Safety/HazardLog Log version: 1/3 |  | 
Identified Hazard | Insulin overdose delivered to patient |  |  |  |  | 
Identified by | Jane Williams |  |  |  |  | 
Criticality class | 1 |  |  |  |  | 
Identified risk | High |  |  |  |  | 
Fault tree identified | YES | Date | 24.01.07 |  | Location | Hazard Log, Page 5
Fault tree creators | Jane Williams and Bill Smith |  |  |  |  | 
Fault tree checked | YES | Date | 28.01.07 |  | Checker | James Brown

## Slide 42: Hazard log (2)
System safety design requirements |  |  |  |  |  | 
1. The system shall include self-testing software that will test the sensor system, the clock, and the insulin delivery system. |  |  |  |  |  | 
2. The self-checking software shall be executed once per minute. |  |  |  |  |  | 
3. In the event of the self-checking software discovering a fault in any of the system components, an audible warning shall be issued and the pump display shall indicate the name of the component where the fault has been discovered. The delivery of insulin shall be suspended. |  |  |  |  |  | 
4. The system shall incorporate an override system that allows the system user to modify the computed dose of insulin that is to be delivered by the system. |  |  |  |  |  | 
5. The amount of override shall be no greater than a pre-set value (maxOverride), which is set when the system is configured by medical staff. |  |  |  |  |  | 

## Slide 43: Safety reviews
Driven by the hazard register.
For each identified hazrd, the review team should assess the system and judge whether or not the system can cope with that hazard in a safe way.

## Slide 44: Formal verification
Formal methods can be used when a mathematical specification of the system is produced.
They are the ultimate static verification technique that may be used at different stages in the development process:
  A formal specification may be developed and mathematically analyzed for consistency. This helps discover specification errors and omissions.
  Formal arguments that a program conforms to its mathematical specification may be developed. This is effective in discovering programming and design errors.

## Slide 45: Arguments for formal methods
Producing a mathematical specification requires a detailed analysis of the requirements and this is likely to uncover errors.
Concurrent systems can be analysed to discover race conditions that might lead to deadlock. Testing for such problems is very difficult.
They can detect implementation errors before testing when the program is analyzed alongside the specification.

## Slide 46: Arguments against formal methods
Require specialized notations that cannot be understood by domain experts.
Very expensive to develop a specification and even more expensive to show that a program meets that specification.
Proofs may contain errors.
It may be possible to reach the same level of confidence in a program more cheaply using other V & V techniques.

## Slide 47: Formal methods cannot guarantee safety
The specification may not reflect the real requirements of system users. Users rarely understand formal notations so they cannot directly read the formal specification to find errors and omissions.
The proof may contain errors. Program proofs are large and complex, so, like large and complex programs, they usually contain errors.
The proof may make incorrect assumptions about the way that the system is used. If the system is not used as anticipated, then the system’s behavior lies outside the scope of the proof.

## Slide 48: Model checking
Involves creating an extended finite state model of a system and, using a specialized system (a model checker), checking that model for errors.
The model checker explores all possible paths through the model and checks that a user-specified property is valid for each path.
Model checking is particularly valuable for verifying concurrent systems, which are hard to test.
Although model checking is computationally very expensive, it is now practical to use it in the verification of small to medium sized critical systems.

## Slide 49: Model checking

## Slide 50: Static program analysis
Static analysers are software tools for source text processing.
They parse the program text and try to discover potentially erroneous conditions and bring these to the attention of the V & V team.
They are very effective as an aid to inspections - they are a supplement to but not a replacement for inspections.

## Slide 51: Automated static analysis checks
Fault class | Static analysis check
Data faults | Variables used before initialization Variables declared but never used Variables assigned twice but never used between assignments Possible array bound violations Undeclared variables
Control faults | Unreachable code Unconditional branches into loops
Input/output faults | Variables output twice with no intervening assignment
Interface faults | Parameter-type mismatches Parameter number mismatches Non-usage of the results of functions Uncalled functions and procedures
Storage management faults | Unassigned pointers Pointer arithmetic Memory leaks

## Slide 52: Levels of static analysis
Characteristic error checking
  The static analyzer can check for patterns in the code that are characteristic of errors made by programmers using a particular language.
User-defined error checking
  Users of a programming language define error patterns, thus extending the types of error that can be detected. This allows specific rules that apply to a program to be checked.
Assertion checking
  Developers include formal assertions in their program and relationships that must hold. The static analyzer symbolically executes the code and highlights potential problems.

## Slide 53: Use of static analysis
Particularly valuable when a language such as C is used which has weak typing and hence many errors are undetected by the compiler.
Particularly valuable for security checking – the static analyzer can discover areas of vulnerability such as buffer overflows or unchecked inputs.
Static analysis is now routinely used in the development of many safety and security critical systems.

## Slide 54: Safety cases

## Slide 55: Safety and dependability cases
Safety and dependability cases are structured documents that set out detailed arguments and evidence that a required level of safety or dependability has been achieved.
They are normally required by regulators before a system can be certified for operational use. The regulator’s responsibility is to check that a system is as safe or dependable as is practical.
Regulators and developers work together and negotiate what needs to be included in a system safety/dependability case.

## Slide 56: The system safety case
A safety case is:
  A documented body of evidence that provides a convincing and valid argument that a system is adequately safe for a given application in a given environment.
Arguments in a safety case can be based on formal proof, design rationale, safety proofs, etc. Process factors may also be included.
A software safety case is usually part of a wider system safety case that takes hardware and operational issues into account.

## Slide 57: The contents of a software safety case
Chapter | Description
System description | An overview of the system and a description of its critical components.
Safety requirements | The safety requirements abstracted from the system requirements specification. Details of other relevant system requirements may also be included.
Hazard and risk analysis | Documents describing the hazards and risks that have been identified and the measures taken to reduce risk. Hazard analyses and hazard logs.
Design analysis | A set of structured arguments (see Section 15.5.1) that justify why the design is safe.
Verification and validation | A description of the V & V procedures used and, where appropriate, the test plans for the system. Summaries of the test results showing defects that have been detected and corrected. If formal methods have been used, a formal system specification and any analyses of that specification. Records of static analyses of the source code.

## Slide 58
Chapter | Description
Review reports | Records of all design and safety reviews.
Team competences | Evidence of the competence of all of the team involved in safety-related systems development and validation.
Process QA | Records of the quality assurance processes (see Chapter 24) carried out during system development.
Change management processes | Records of all changes proposed, actions taken and, where appropriate, justification of the safety of these changes. Information about configuration management procedures and configuration management logs.
Associated safety cases | References to other safety cases that may impact the safety case.

## Slide 59: Structured arguments
Safety cases should be based around structured arguments that present evidence to justify the assertions made in these arguments.
The argument justifies why a claim about system safety and security is justified by the available evidence.

## Slide 60: Structured arguments

## Slide 61: Insulin pump safety argument
Arguments are based on claims and evidence.
Insulin pump safety:
  Claim: The maximum single dose of insulin to be delivered (CurrentDose) will not exceed MaxDose.
  Evidence: Safety argument for insulin pump (discussed later)
  Evidence: Test data for insulin pump. The value of currentDose was correctly computed in 400 tests
  Evidence: Static analysis report for insulin pump software revealed no anomalies that affected the value of CurrentDose
  Argument: The evidence presented demonstrates that the maximum dose of insulin that can be computed = MaxDose.

## Slide 62: Structured safety arguments
Structured arguments that demonstrate that a system meets its safety obligations.
It is not necessary to demonstrate that the program works as intended; the aim is simply to demonstrate safety.
Generally based on a claim hierarchy.
  You start at the leaves of the hierarchy and demonstrate safety. This implies the higher-level claims are true.

## Slide 63: A safety claim hierarchy for the insulin pump

## Slide 64: Software safety arguments
Safety arguments are intended to show that the system cannot reach in unsafe state.
These are weaker than correctness arguments which must show that the system code conforms to its specification.
They are generally based on proof by contradiction
  Assume that an unsafe state can be reached;
  Show that this is contradicted by the program code.
A graphical model of the safety argument may be developed.

## Slide 65: Construction of a safety argument
Establish the safe exit conditions for a component or a program.
Starting from the END of the code, work backwards until you have identified all paths that lead to the exit of the code.
Assume that the exit condition is false.
Show that, for each path leading to the exit that the assignments made in that path contradict the assumption of an unsafe exit from the component.

## Slide 66: Insulin dose computation with safety checks
-- The insulin dose to be delivered is a function of blood sugar level,
-- the previous dose delivered and the time of delivery of the previous dose
currentDose = computeInsulin () ;
// Safety check—adjust currentDose if necessary.
// if statement 1
if (previousDose == 0)
{
if (currentDose > maxDose/2)
currentDose = maxDose/2 ;
}
else
if (currentDose > (previousDose * 2) )
currentDose = previousDose * 2 ;
// if statement 2
if ( currentDose < minimumDose )
currentDose = 0 ;
else if ( currentDose > maxDose )
currentDose = maxDose ;
administerInsulin (currentDose) ;

## Slide 67: Informal safety argument based on demonstrating contradictions

## Slide 68: Program paths
Neither branch of if-statement 2 is executed
  Can only happen if CurrentDose is >= minimumDose and <= maxDose.
then branch of if-statement 2 is executed
  currentDose = 0.
else branch of if-statement 2 is executed
  currentDose = maxDose.
In all cases, the post conditions contradict the unsafe condition that the dose administered is greater than maxDose.

## Slide 69: Key points
Safety-critical systems are systems whose failure can lead to human injury or death.
A hazard-driven approach is used to understand the safety requirements for safety-critical systems. You identify potential hazards and decompose these (using methods such as fault tree analysis) to discover their root causes. You then specify requirements to avoid or recover from these problems.
It is important to have a well-defined, certified process for safety-critical systems development. This should include the identification and monitoring of potential hazards.

## Slide 70: Key points
Static analysis is an approach to V & V that examines the source code of a system, looking for errors and anomalies. It allows all parts of a program to be checked, not just those parts that are exercised by system tests.
Model checking is a formal approach to static analysis that exhaustively checks all states in a system for potential errors.
Safety and dependability cases collect the evidence that demonstrates a system is safe and dependable. Safety cases are required when an external regulator must certify the system before it is used.