## Slide 1: Chapter 21– Real-time Software Engineering

## Slide 2: Topics covered
Embedded system design
Architectural patterns for real-time software
Timing analysis
Real-time operating systems

## Slide 3: Embedded software
Computers are used to control a wide range of systems from simple domestic machines, through games controllers, to entire manufacturing plants.
Their software must react to events generated by the hardware and, often, issue control signals in response to these events.
The software in these systems is embedded in system hardware, often in read-only memory, and usually responds, in real time, to events from the system’s environment.

## Slide 4: Responsiveness
Responsiveness in real-time is the critical difference between embedded systems and other software systems, such as information systems, web-based systems or personal software systems.
For non-real-time systems, correctness can be defined by specifying how system inputs map to corresponding outputs that should be produced by the system.
In a real-time system, the correctness depends both on the response to an input and the time taken to generate that response. If the system takes too long to respond, then the required response may be ineffective.

## Slide 5: Definition
A real-time system is a software system where the correct functioning of the system depends on the results produced by the system and the time at which these results are produced.
A soft real-time system is a system whose operation is degraded if results are not produced according to the specified timing requirements.
A hard real-time system is a system whose operation is incorrect if results are not produced according to the timing specification.

## Slide 6: Characteristics of embedded systems
Embedded systems generally run continuously and do not terminate.
Interactions with the system’s environment are unpredictable.
There may be physical limitations that affect the design of a system.
Direct hardware interaction may be necessary.
Issues of safety and reliability may dominate the system design.

## Slide 7: Embedded system design

## Slide 8: Embedded system design
The design process for embedded systems is a systems engineering process that has to consider, in detail, the design and performance of the system hardware.
Part of the design process may involve deciding which system capabilities are to be implemented in software and which in hardware.
Low-level decisions on hardware, support software and system timing must be considered early in the process.
These may mean that additional software functionality, such as battery and power management, has to be included in the system.

## Slide 9: Reactive systems
Real-time systems are often considered to be reactive systems. Given a stimulus, the system must produce a reaction or response within a specified time.
Periodic stimuli. Stimuli which occur at predictable time intervals
  For example, a temperature sensor may be polled 10 times per second.
Aperiodic stimuli. Stimuli which occur at unpredictable times
  For example, a system power failure may trigger an interrupt which must be processed by the system.

## Slide 10: Stimuli and responses for a burglar alarm system
Stimulus | Response
Clear alarms | Switch off all active alarms; switch off all lights that have been switched on.
Console panic button positive | Initiate alarm; turn on lights around console; call police.
Power supply failure | Call service technician.
Sensor failure | Call service technician.
Single sensor positive | Initiate alarm; turn on lights around site of positive sensor.
Two or more sensors positive | Initiate alarm; turn on lights around sites of positive sensors; call police with location of suspected break-in.
Voltage drop of between 10% and 20% | Switch to battery backup; run power supply test.
Voltage drop of more than 20% | Switch to battery backup; initiate alarm; call police; run power supply test.

## Slide 11: Types of stimuli
Stimuli come from sensors in the systems environment and from actuators controlled by the system
  Periodic stimuli These occur at predictable time intervals.
  For example, the system may examine a sensor every 50 milliseconds and take action (respond) depending on that sensor value (the stimulus).
  Aperiodic stimuli These occur irregularly and unpredictably and are may be signalled using the computer’s interrupt mechanism.
  An example of such a stimulus would be an interrupt indicating that an I/O transfer was complete and that data was available in a buffer.

## Slide 12: A general model of an embedded real-time system

## Slide 13: Architectural considerations
Because of the need to respond to timing demands made by different stimuli/responses, the system architecture must allow for fast switching between stimulus handlers.
Timing demands of different stimuli are different so a simple sequential loop is not usually adequate.
Real-time systems are therefore usually designed as cooperating processes with a real-time executive controlling these processes.

## Slide 14: Sensor and actuator processes

## Slide 15: System elements
Sensor control processes
  Collect information from sensors. May buffer information collected in response to a sensor stimulus.
Data processor
  Carries out processing of collected information and computes the system response.
Actuator control processes
  Generates control signals for the actuators.

## Slide 16: Design process activities
Platform selection
Stimuli/response identification
Timing analysis
Process design
Algorithm design
Data design
Process scheduling

## Slide 17: Process coordination
Processes in a real-time system have to be coordinated and share information.
Process coordination mechanisms ensure mutual exclusion to shared resources.
When one process is modifying a shared resource, other processes should not be able to change that resource.
When designing the information exchange between processes, you have to take into account the fact that these processes may be running at different speeds.

## Slide 18: Mutual exclusion
Producer processes collect data and add it to the buffer. Consumer processes take data from the buffer and make elements available.
Producer and consumer processes must be mutually excluded from accessing the same element.
The buffer must stop producer processes adding information to a full buffer and consumer processes trying to take information from an empty buffer.

## Slide 19: Producer/consumer processes sharing a circular buffer

## Slide 20: Real-time system modelling
The effect of a stimulus in a real-time system may trigger a transition from one state to another.
State models are therefore often used to describe embedded real-time systems.
UML state diagrams may be used to show the states and state transitions in a real-time system.

## Slide 21: State machine model of a petrol (gas) pump

## Slide 22: Sequence of actions in real-time pump control system
The buyer inserts a credit card into a card reader built into the pump.
Removal of the card triggers a transition to a Validating state where the card is validated.
If the card is valid, the system initializes the pump and, when the fuel hose is removed from its holster, transitions to the Delivering state.
After the fuel delivery is complete and the hose replaced in its holster, the system moves to a Paying state.
After payment, the pump software returns to the Waiting state

## Slide 23: Real-time programming
Programming languages for real-time systems development have to include facilities to access system hardware, and it should be possible to predict the timing of particular operations in these languages.
Systems-level languages, such as C, which allow efficient code to be generated are widely used in preference to languages such as Java.
There is a performance overhead in object-oriented systems because extra code is required to mediate access to attributes and handle calls to operations. The loss of performance may make it impossible to meet real-time deadlines.

## Slide 24: Architectural patterns for real-time software

## Slide 25: Architectural patterns for embedded systems
Characteristic system architectures for embedded systems
  Observe and React This pattern is used when a set of sensors are routinely monitored and displayed.
  Environmental Control This pattern is used when a system includes sensors, which provide information about the environment and actuators that can change the environment
  Process Pipeline This pattern is used when data has to be transformed from one representation to another before it can be processed.

## Slide 26: The Observe and React pattern
Name | Observe and React
Description | The input values of a set of sensors of the same types are collected and analyzed. These values are displayed in some way. If the sensor values indicate that some exceptional condition has arisen, then actions are initiated to draw the operator’s attention to that value and, in certain cases, to take actions in response to the exceptional value.
Stimuli | Values from sensors attached to the system.
Responses | Outputs to display, alarm triggers, signals to reacting systems.
Processes | Observer, Analysis, Display, Alarm, Reactor.
Used in | Monitoring systems, alarm systems.

## Slide 27: Observe and React process structure

## Slide 28: Alarm system description
A software system is to be implemented as part of a burglar alarm system for commercial buildings. This uses several different types of sensor. These include movement detectors in individual rooms, door sensors that detect corridor doors opening, and window sensors on ground-floor windows that detect when a window has been opened.
When a sensor detects the presence of an intruder, the system automatically calls the local police and, using a voice synthesizer, reports the location of the alarm. It switches on lights in the rooms around the active sensor and sets off an audible alarm. The sensor system is normally powered by mains power but is equipped with a battery backup. Power loss is detected using a separate power circuit monitor that monitors the mains voltage. If a voltage drop is detected, the system assumes that intruders have interrupted the power supply so an alarm is raised.

## Slide 29: Process structure for a burglar alarm system

## Slide 30: The Environmental Control pattern
Name | Environmental Control
Description | The system analyzes information from a set of sensors that collect data from the system’s environment. Further information may also be collected on the state of the actuators that are connected to the system. Based on the data from the sensors and actuators, control signals are sent to the actuators that then cause changes to the system’s environment. Information about the sensor values and the state of the actuators may be displayed.
Stimuli | Values from sensors attached to the system and the state of the system actuators.
Responses | Control signals to actuators, display information.
Processes | Monitor, Control, Display, Actuator Driver, Actuator monitor.
Used in | Control systems.

## Slide 31: Environmental Control process structure

## Slide 32: Control system architecture for an anti-skid braking system

## Slide 33: The Process Pipeline pattern
Name | Process Pipeline
Description | A pipeline of processes is set up with data moving in sequence from one end of the pipeline to another. The processes are often linked by synchronized buffers to allow the producer and consumer processes to run at different speeds. The culmination of a pipeline may be display or data storage or the pipeline may terminate in an actuator.
Stimuli | Input values from the environment or some other process
Responses | Output values to the environment or a shared buffer
Processes | Producer, Buffer, Consumer
Used in | Data acquisition systems, multimedia systems

## Slide 34: Process Pipeline process structure

## Slide 35: Neutron flux data acquisition

## Slide 36: Timing analysis

## Slide 37: Timing analysis
The correctness of a real-time system depends not just on the correctness of its outputs but also on the time at which these outputs were produced.
In a timing analysis, you calculate how often each process in the system must be executed to ensure that all inputs are processed and all system responses produced in a timely way.
The results of the timing analysis are used to decide how frequently each process should execute and how these processes should be scheduled by the real-time operating system.

## Slide 38: Factors in timing analysis
Deadlines
  The times by which stimuli must be processed and some response produced by the system.
Frequency
  The number of times per second that a process must execute so that you are confident that it can always meet its deadlines.
Execution time
  The time required to process a stimulus and produce a response.

## Slide 39: Power failure timing analysis

## Slide 40: Power failure timings
It takes 50 milliseconds (ms) for the supplied voltage to drop to a level where the equipment may be damaged. The battery backup must therefore be activated and in operation within 50ms.
It takes 16ms from starting the backup power supply to the supply being fully operational.
There is a checking process that is scheduled to run 250 times per second i.e. every 4ms.
  This process assumes that there is a power supply problem if there is a significant drop in voltage between readings and this is sustained for 3 readings.

## Slide 41: Power failure timings
Assume the power fails immediately after a reading has been taken. Therefore reading R1 is the start reading for the power fail check. The voltage continues to drop for readings R2­–R4, so a power failure is assumed. This is the worst possible case.
At this stage, the process to switch to the battery backup is started. Because the battery backup takes 16ms to become operational, this means that the worst-case execution time for this process is 8ms.

## Slide 42: Timing requirements for the burglar alarm system
Stimulus/Response | Timing requirements
Audible alarm | The audible alarm should be switched on within half a second of an alarm being raised by a sensor.
Communications | The call to the police should be started within 2 seconds of an alarm being raised by a sensor.
Door alarm | Each door alarm should be polled twice per second.
Lights switch | The lights should be switched on within half a second of an alarm being raised by a sensor.
Movement detector | Each movement detector should be polled twice per second.
Power failure | The switch to backup power must be completed within a deadline of 50 ms.
Voice synthesizer | A synthesized message should be available within 2 seconds of an alarm being raised by a sensor.
Window alarm | Each window alarm should be polled twice per second.

## Slide 43: Alarm process timing

## Slide 44: Stimuli to be processed
Power failure is detected by observing a voltage drop of more than 20%.
  The required response is to switch the circuit to backup power by signalling an electronic power-switching device that switches the mains power to battery backup.
Intruder alarm is a stimulus generated by one of the system sensors.
  The response to this stimulus is to compute the room number of the active sensor, set up a call to the police, initiate the voice synthesizer to manage the call, and switch on the audible intruder alarm and building lights in the area.

## Slide 45: Frequency and execution time
The deadline for detecting a change of state is 0.25 seconds, which means that each sensor has to be checked 4 times per second. If you examine 1 sensor during each process execution, then if there are N sensors of a particular type, you must schedule the process 4N times per second to ensure that all sensors are checked within the deadline.
If you examine 4 sensors, say, during each process execution, then the execution time is increased to about 4 ms, but you need only run the process N times/second to meet the timing requirement.

## Slide 46: Real-time operating systems

## Slide 47: Real-time operating systems
Real-time operating systems are specialised operating systems which manage the processes in the RTS.
Responsible for process management and resource (processor and memory) allocation.
May be based on a standard kernel which is used unchanged or modified for a particular application.
Do not normally include facilities such as file management.

## Slide 48: Operating system components
Real-time clock
  Provides information for process scheduling.
Interrupt handler
  Manages aperiodic requests for service.
Scheduler
  Chooses the next process to be run.
Resource manager
  Allocates memory and processor resources.
Dispatcher
  Starts process execution.

## Slide 49: Non-stop system components
Configuration manager
  Responsible for the dynamic reconfiguration of the system software and hardware. Hardware modules may be replaced and software upgraded without stopping the systems.
Fault manager
  Responsible for detecting software and hardware faults and taking appropriate actions (e.g. switching to backup disks) to ensure that the system continues in operation.

## Slide 50: Components of a real-time operating system

## Slide 51: Process management
Concerned with managing the set of concurrent processes.
Periodic processes are executed at pre-specified time intervals.
The RTOS uses the real-time clock to determine when to execute a process taking into account:
  Process period - time between executions.
  Process deadline - the time by which processing must be complete.

## Slide 52: Process management
The processing of some types of stimuli must sometimes take priority.
Interrupt level priority. Highest priority which is allocated to processes requiring a very fast response.
Clock level priority. Allocated to periodic processes.
Within these, further levels of priority may be assigned.

## Slide 53: Interrupt servicing
Control is transferred automatically to a pre-determined memory location.
This location contains an instruction to jump to an interrupt service routine.
Further interrupts are disabled, the interrupt serviced and control returned to the interrupted process.
Interrupt service routines MUST be short, simple and fast.

## Slide 54: Periodic process servicing
In most real-time systems, there will be several classes of periodic process, each with different periods (the time between executions), execution times and deadlines (the time by which processing must be completed).
The real-time clock ticks periodically and each tick causes an interrupt which schedules the process manager for periodic processes.
The process manager selects a process which is ready for execution.

## Slide 55: RTOS actions required to start a process

## Slide 56: Process switching
The scheduler chooses the next process to be executed by the processor. This depends on a scheduling strategy which may take the process priority into account.
The resource manager allocates memory and a processor for the process to be executed.
The dispatcher takes the process from ready list, loads it onto a processor and starts execution.

## Slide 57: Scheduling strategies
Non pre-emptive scheduling
  Once a process has been scheduled for execution, it runs to completion or until it is blocked for some reason (e.g. waiting for I/O).
Pre-emptive scheduling
  The execution of an executing processes may be stopped if a higher priority process requires service.
Scheduling algorithms
  Round-robin;
  Rate monotonic;
  Shortest deadline first.

## Slide 58: Key points
An embedded software system is part of a hardware/software system that reacts to events in its environment. The software is ‘embedded’ in the hardware. Embedded systems are normally real-time systems.
A real-time system is a software system that must respond to events in real time. System correctness does not just depend on the results it produces, but also on the time when these results are produced.
Real-time systems are usually implemented as a set of communicating processes that react to stimuli to produce responses.
State models are an important design representation for embedded real-time systems. They are used to show how the system reacts to its environment as events trigger changes of state in the system.

## Slide 59: Key points
There are several standard patterns that can be observed in different types of embedded system. These include a pattern for monitoring the system’s environment for adverse events, a pattern for actuator control and a data-processing pattern.
Designers of real-time systems have to do a timing analysis, which is driven by the deadlines for processing and responding to stimuli. They have to decide how often each process in the system should run and the expected and worst-case execution time for processes.
A real-time operating system is responsible for process and resource management. It always includes a scheduler, which is the component responsible for deciding which process should be scheduled for execution.